## Slide 1: Scheduling Problems and Algorithms in Traffic and Transport
MAPSP 2011 Nymburk, 24.06.11
Ralf Borndörfer Zuse-Institute Berlin
Joint work with Ivan Dovica, Martin Grötschel, Olga Heismann, Andreas Löbel, Markus Reuther, Elmar Swarat, Thomas Schlechte, Steffen Weider

## Slide 2: Optimization in Public Transit
Duty
Scheduling
Fare Planning
Duty Rostering
Integrated Scheduling
Line Planning
Trip Scheduling
Depot Scheduling
Vehicle Scheduling

## Slide 3: Railway Challenges
Trip 1
Trip 2
Trip 4
Trip 5
Trip 3
Trip 6
Trip 7
  Basic Rolling Stock Rostering Problem = Multicommodity Flow Problem
  Can be solved efficiently for networks with 109 arcs
  Constraints complicating rolling stock rostering
  Discretization: Space/Time ("Multiscale Problems")
  Robustness: Delay Propagation
  Path Constraints: Maintenance, Parking
  Configuration Constraints: Track Usage, Train Composition, Uniformity
Photo courtesy of DB Mobility Logistics AG
We want to avoid this!
Simplon Tunnel
Visualization based on JavaView
Notes: Railways = Source of Challenging Combinatorial Optimization Problems. Research needed.

## Slide 4
Integrated Routing and Scheduling

## Slide 5: Integrated Routing and Scheduling
Routing
Scheduling

## Slide 6: Timetable

## Slide 7: Train Routes are Flexible in Space and Time

## Slide 8: Conflict

## Slide 9: Track Allocation Graph

## Slide 10: Track Allocation/Train Timetabling Problem
Combinatorial Optimization Problem
  Path Packing Problem
…

## Slide 11: Literature
  Charnes and Miller (1956), Szpigel (1973), Jovanovic and Harker (1991),
  Cai and Goh (1994), Schrijver and Steenbeck (1994), Carey and Lockwood (1995)
  Nachtigall and Voget (1996), Odijk (1996) Higgings, Kozan and Ferreira (1997)
  Brannlund, Lindberg, Nou, Nilsson (1998), Lindner (2000), Oliveira and Smith (2000)
  Caprara, Fischetti and Toth (2002), Peeters (2003)
  Kroon and Peeters (2003), Mistry and Kwan (2004)
  Barber, Salido, Ingolotti, Abril, Lova, Tormas (2004)
  Semet and Schoenauer (2005),
  Caprara, Monaci, Toth and Guida (2005)
  Kroon, Dekker and Vromans (2005),
  Vansteenwegen and Van Oudheusden (2006), Liebchen (2006)
  Cacchiani, Caprara, T. (2006), Cachhiani (2007)
  Caprara, Kroon, Monaci, Peeters, Toth (2006)
  Borndoerfer, Schlechte (2005, 2007), Caimi G., Fuchsberger M., Laumanns M., Schüpbach K. (2007)
  Fischer, Helmberg, Janßen, Krostitz (2008)
  Lusby, Larsen, Ehrgott, Ryan (2009)
  Caimi (2009), Klabes (2010)
  ...

## Slide 12: Path/Arc Packing Model

## Slide 13: Path Packing Model

## Slide 14: Configuration Model

## Slide 15: Configuration Model

## Slide 16: Packing- and Configuration Model

## Slide 17: Track Allocation Models
Theorem (B., Schlechte [2007]):
= vLP(PCP) = vLP(ACP)
= vLP (APP) = vLP(PPP)
≤ vLP(APP').
All LP-relaxations can be solved in polynomial time.
= vIP(PCP) = vIP(ACP)
= vIP (APP) = vIP(PPP)
= vIP(APP').
APP
ACP
PCP
PPP
APP'

## Slide 18: Packing- and Configuration Model

## Slide 19: Configuration Model

## Slide 20: Configuration Model
Proposition: Route pricing = acyclic shortest path problem with arc weights ca = ca+a.

## Slide 21: Configuration Model
Proposition: Config pricing = acyclic shortest path problem with arc weights ca = a.

## Slide 22: Configuration Model

## Slide 23: Lagrange Funktion des PCP
(PCP)
(LD)

## Slide 24: Bundle Method (Kiwiel [1990], Helmberg [2000])
  Problem
  Algorithm
    Subgradient
    Cutting Plane Model
    Update
  Quadratic Subproblem
  Primal Approximation
  Inexact Bundle Method

f
Notes: We will now take a closer look, at the determination of the next trial point

## Slide 25: Bundle Method (Kiwiel [1990], Helmberg [2000])
  Problem
  Algorithm
    Subgradient
    Cutting Plane Model
    Update
  Quadratic Subproblem
  Primal Approximation
  Inexact Bundle Method

f
1
Notes: We will now take a closer look, at the determination of the next trial point

## Slide 26: Bundle Method (Kiwiel [1990], Helmberg [2000])

f
1
2
  Problem
  Algorithm
    Subgradient
    Cutting Plane Model
    Update
  Quadratic Subproblem
  Primal Approximation
  Inexact Bundle Method
Notes: We will now take a closer look, at the determination of the next trial point

## Slide 27: Bundle Method (Kiwiel [1990], Helmberg [2000])

f
1
2
3
  Problem
  Algorithm
    Subgradient
    Cutting Plane Model
    Update
  Quadratic Subproblem
  Primal Approximation
  Inexact Bundle Method
Notes: We will now take a closer look, at the determination of the next trial point

## Slide 28: Bundle Method (Kiwiel [1990], Helmberg [2000])
1
2
3
  Problem
  Algorithm
    Subgradient
    Cutting Plane Model
    Update
  Quadratic Subproblem
  Primal Approximation
  Inexact Bundle Method
Notes: We will now take a closer look, at the determination of the next trial point

## Slide 29: Rapid Branching
Perturbation Branching
  Sequence of perturbed IP objectives cji+1 := cji – (xji)2, j, i=1,2,…
  Fixing candidates in iteration i Bi := { j : xji  1 –  }
  Potential function in iteration i vi := cTxi – w|Bi |
  Go on while not integer and potential decreases, else
    Perturb for kmax additional iterations, if still not successful
      Fix a single variable and reset objective every ks iterations
  Set of fixed variables (many) B* := Bargmin vi
Binary Search Branching
  Set of fixed variables (many) B* := {j1, ... , jm}, cj1  ...  cjm
  Sets Qjk at pertubation branch j Qjk := { x : xj1=...=xjk=1 }, k=0,...,m
  Branch on Qjm
    Repeat perturbation branching to plunge
    Backtrack to Qjm/2 and set m := m/2 to prune
29
Qj2
Qjm/4
Qjm/2
Qjm
Qj-1p/q
Qj1
Qj4

## Slide 30: A Simple LP-Bound
Lemma (BS [2007]):

## Slide 31: Solving the LP-Relaxation

## Slide 32: Solving the IP
Mathematische Optimierung
  HaKaFu, req32, 1140 requests, 30 mins time windows

## Slide 33: Track Allocation and Train Timetabling
Mathematische Optimierung
  BAB: Branch-and-Bound
  PAB: Price-and-Branch
  BAP: Branch-and-Price
Article | Stations | Tracks | Trains | Modell/Approach
Szpigel [1973] | 6 | 5 | 10 | Packing/Enumeration
Brännlund et al. [1998] | 17 | 16 | 26 | Packing/ Lagrange, BAB
Caprara et al. [2002] | 74 (17) | 73 (16) | 54 (221) | Packing/ Lagrange, BAB
B. & Schlechte [2007] | 37 | 120 | 570 | Config/PAB
Caprara et al. [2007] | 102 (16) | 103 (17) | 16 (221) | Packing/PAB
Fischer et al. [2008] | 656 (104) | 1210 (193) | 117 (251) | Packing/Bundle, IP Rounding
Lusby et al. [2008] | ??? | 524 | 66 (31) | Packing/BAP
B. & Schlechte [2010] | 37 | 120 | >1.000 | Config/Rapid Branching

## Slide 34
Discretization and Scheduling

## Slide 35: Railway Infrastructure Modeling
  Detailed railway infrastucture data given by simulation programs (Open Track)
  Switches
  Signals
  Tracks (with max. speed, acceleration, gradient)
  Stations and Platforms
Mathematische Optimierung

## Slide 36: Microscopic Model
  Simplon micrograph: 1154 nodes and 1831 arcs, 223 signals etc.
Mathematische Optimierung
Notes: 36

## Slide 37: Headways
  Simulation tools provide exact running and blocking times
  Basis for calculation of minimal headway times
Mathematische Optimierung

## Slide 38: Macroscopic Network Generation
38
  Simulation of all possible routes with appropiate train types
EC
R
GV Auto Brig-Iselle
GV ROLA
GV SIM
GV MTO
Chosen TrainTypes
BRTU
SGAA
IS_A
IS
BRRB
BR
VAR
MOGN
PRE
DOFM
DO
DOBI_A
Mathematische Optimierung

## Slide 39: Interaction of Train Routes
  Generation of artifical nodes – „pseudo“ stations
  No interactions between train routes
IS
  Macro network definition is based on set of train routes
Mathematische Optimierung

## Slide 40: Interaction of Train Routes
  Generation of artifical nodes – „pseudo“ stations
  Diverging of train routes
IS_P
IS
  The same holds for converging routes
Mathematische Optimierung

## Slide 41: Interaction of Train Routes
  Generation of artifical nodes – pseudo stations
  crossing of train routes
IS_P1
IS
IS_P2
  Two pseudo stations were generated
Mathematische Optimierung

## Slide 42: Reduced Macrograph (53 nodes and 87 track arcs for 28 train routes)
Mathematische Optimierung
Notes: 42

## Slide 43: Station Aggregation
  Frequently many macroscopic station nodes are in the area of big stations
  Further aggregation is needed
k
k
k =
EC | 2
R | 4
GV Auto | 2
GV Rola | 2
GV SIM | 4
GV MTO | 6
Mathematische Optimierung
Notes: 43

## Slide 44: Micro-Macro Transformation
  Planned times in macro network are possible in micro network
  Valid headways lead to valid block occupations (no conflicts)
   feasible macro timetable can be transformed to feasible micro timetable
Mathematische Optimierung

## Slide 45: Micro-Macro-Transformation: Simplon Case
Micro
12 stations
1154 OpenTrack nodes
1831 OpenTrack edges
223 signals
8 track junctions
100 switches
6 train types
28 “routes“
230 ”block segments“
Macro
18 macro nodes
40 tracks
6 Train types
Mathematische Optimierung

## Slide 46: Time Discretization
  Cumulative Rounding Procedure
  Compute macroscopic running time with specific rounding procedure
  Consider again routes of trains (represented by standard trains)
  Example with
Station | Dep/Pass | Rounded | Buffer
A | 0 | 0 | 0
B | 11 | 12 (2) | 1
C | 20 | 24 (4) | 4
D | 29 | 30 (5) | 1
  Theorem: If micro-running time d   for all tracks of the current train route, the cumulative rounding error (buffer) is always in .
Mathematische Optimierung

## Slide 47: Complex Traffic at the Simplon
Slalom route
  ROLA trains traverse the tunnel on the “wrong“ side
Crossing of trains
  complex crossings of AUTO trains in Iselle
Conflicting routes
  complex routings in station area Domodossola and Brig
Source: Wikipedia
Mathematische Optimierung

## Slide 48: Dense Traffic at the Simplon
Chart: 
| 00-04 | 04-08 | 08-12 | 12-16 | 16-20 | 20-24
Sum | 12 | 22 | 28 | 20 | 24 | 20
PV | 6 | 11 | 14 | 10 | 12 | 10
EC | 5 | 2 | 8 | 4 | 4 | 6
GV Auto | 0 | 4 | 5 | 5 | 6 | 4
R | 1 | 5 | 1 | 1 | 2 | 0

## Slide 49: Saturation
Estimation of the maximum theoretical corridor capacity
  Network accuracy of 6s
  Consider complete routing through stations
  Saturate by additional cargo trains
  Conflict free train schedules in simulation software (1s accuracy)

## Slide 50: Manual Reference Plan
  Aggregation-Test (Micro->Macro->Micro)
  Microscopic feasible 4h (8:00-12:00) reference plan in Open Track
  Reproducing this plan by an Optimization run
  Reimport to Open Track

## Slide 51: Theoretical Capacities
  180 trains for network small (without station routing and buffer times)
  196 trains for network big with precise routing through stations (without buffer times)
  175 trains for network big with precise routing through stations and buffer times

## Slide 52: Retransformation to Microscopic Level (Network big)
  No delays, no early coming
  Feasible train routing and block occupation
  Timetable is valid in micro-simulation
52

## Slide 53: Valid blocking time stairs
53
  Network big with buffer times

## Slide 54: Time Discretization Analysis
  Network big with buffer times
54
Time discretization dt/s | 6 | 10 | 30 | 60
Number of trains | 196 | 187 | 166 | 146
Cols in IP | 504314 | 318303 | 114934 | 61966
Rows in IP | 222096 | 142723 | 53311 | 29523
Solution time in secs | 72774.55 | 12409.19 | 110.34 | 10.30

## Slide 55
Hypergraph Scheduling

## Slide 56: Trip Network

## Slide 57: Cyclic Timetable for Standard Week
57
(Visualization based on JavaView)
Notes: 57

## Slide 58: Rotation

## Slide 59: Rotation

## Slide 60: Rotation Schedule (Blue: Timetable, Red: Deadheads)
(Visualization based on JavaView)

## Slide 61: (Operational) Uniformity

## Slide 62: Uniformity (Blue: Uniform, …, Red: Irregular)
62
(Visualization based on JavaView)
Notes: 62

## Slide 63: Uniformity (Blue/Yellow: Uniform, …, Red: Irregular, Fat: Maintenance)
(Visualization based on JavaView)

## Slide 64: Rotation Schedule

## Slide 65: Uniformity

## Slide 66: Uniformity

## Slide 67: Modelling Uniformity Using Hyperarcs

## Slide 68: Hyperassignment

## Slide 69: Hyperassignment Problem
Definition: Let D=(V,A) be a directed hypergraph w. arc costs ca
  H⊆A hyperassigment : +(v)H = -(v)H = 1
  Hyperassignment Problem : argmin c(H), H hyperassignment
Literature
  Cambini, Gallo, Scutellà (1992): Minimum cost flows on hypergraphs; solves only the LP relaxation
  Jeroslow, Martin, Rarding, Wang (1992): Gainfree Leontief substitution flow problems; does not hold for the hyperassignment problem
Theorem: The HAP is NP-hard (even for simple cases).

## Slide 70: Further Complexity Results
Theorem: The LP/IP gap of HAP can be arbitrarity large.

## Slide 71: Further Complexity Results
Theorem: The LP/IP gap of HAP can be arbitrarity large.

## Slide 72: Further Complexity Results
Theorem: The LP/IP gap of HAP can be arbitrarity large.

## Slide 73: Further Complexity Results
Theorem: The LP/IP gap of HAP can be arbitrarity large.
Proposition: The determinants of basis matrices of HAP can be arbitrarily large, even if all hyperarcs have head and tail size 2.
Proposition: HAP is APX-complete for hyperarc head and tail size 2 in general and for hyperarc head and tail cardinality 3 in the revelant cases.

## Slide 74: Computational Results (CPLEX 12.1.0)

## Slide 75: Partitioned Hypergraph and Configurations
ICE 4711
(Mo)
ICE 4711
(Tu)
ICE 4711
(Su)
ICE 4711
(Mo)
ICE 4711
(Tu)
ICE 4711
(Su)
ICE 4711
(Mo)
ICE 4711
(Tu)
ICE 4711
(Su)

## Slide 76: Extended Configuration Formulation
Theorem: There is an extended formulation of HAP with O(V8) variables that implies all clique constraints.

## Slide 77
Stochastic Scheduling

## Slide 78: Delays
Cost of delays
  72 €/minute average cost of gate delay over 15 minutes, cf. EUROCONTROL [2004]
  840 – 1200 millions € annual costs caused by gate delays in Europe
Benefits of robust planning
  Cost savings
  Reputation
  Less operational changes
The Tail Assignment Problem – assign legs to aircraft in order to fulfill operational constraints such as preassignments, maintenance rules, airport curfews, and minimum connection times between legs, cf. Grönkvist [2005]
We consider the tail assignment problem in a research project based on real-world data from a European carrier using the NetLine system

## Slide 79: Delay Propagation

## Slide 80: Delay Propagation Along Rotations
EDP (bad)
EDP (good)

## Slide 81: Delay Propagation
Goal: Decrease impact of delays
  Primary delays: genuine disruptions, unavoidable
  Propagated delays: consequences of aircraft routing, can be minimized
Rule-oriented planning
  Ad-hoc formulas for buffers
  These rules are costly and it is uncertain how efficient they are
  Calibrating these rules is a balancing act: supporting operational stability, while staying cost efficient
Goal-oriented planning
  Minimize occurrence of delay propagation on average

## Slide 82: Stochastic Model (similar to Rosenberger et. al. [2002])
Delay distribution
  Delays are not homogeneously spread in the network
  Stochastic model must captures properties of individual airports and legs
Structure of the stochastic model
  Gate phase, representing time spent on the ground
  Flight phase, representing time spent en-route
Phase durations are modelled by probability distribution
  Gj is random variable for delay of gate phase of leg j
  Fj is random variable for duration of flight phase of leg j

## Slide 83: Robust Tail Assignment Problem
Mathematical model:
  Minimize non-robustness
  Cover all legs
  Fulfill side constraints
  One rotation for each aircraft
  Integrality
  Set partitioning problem with side constraints
  Problem has to be resolved daily for period of a few days
  Solved by Netline/Ops Tail xOPT (state-of-the-art column generation solver by Lufthansa Systems)
Notes: R_k contains all preassignments….
side constraints: maintenance….
Rotations for individual aircraft….
D_r is difference between normal and our tail ASS

## Slide 84: Column Generation
Start
Solve Tail Assignment Problem (IP)
Solve Tail Assignment Problem (LP)
Stop?
All fixed?
Stop
Yes
No
Yes
No
Compute rotations
Compute prices
Fix rotations
Conflict? Backtrack?
Yes
No
Notes: Tail is solved by col gen.
This is standard

## Slide 85: Column Generation
Start
Solve Tail Assignment Problem (IP)
Solve Tail Assignment Problem (LP)
Stop?
All fixed?
Stop
Yes
No
Yes
No
Compute
robust rotations
Compute prices
Fix rotations
Conflict? Backtrack?
Yes
No

## Slide 86: Pricing Robust Rotations
  Robustness measure: total probability of delay propagation (PDP)
  Resource constraint shortest path problem
  where is random variable of delay propagated to leg i in rotation r and are dual variables corresponding to cover, aircraft, and side constraints
To solve this problem one must compute along rotations
Notes: I have to say that we compute convolution numerically, otherwise Different approaches does not make sense on this slide!

## Slide 87: Computing PDi Along a Rotation
Delay distribution Hj of leg j
  Hj = Gj + Fj
Delay propagation from leg j to leg k via buffer bjk
  PDk = max( Hj - bjk , 0)
Delay distribution Hk of next leg k
  Hk = PDk + Gk + Fk
and so on…
convolution
convolution
convolution

## Slide 88: Convolution
Convolution
  H = F + G and f, g and h are their probability density functions
Numerical convolution based on discretization
where are stepwise constant approximations of functions f, g
Alternative approaches
  Analytical convolution, cf. Fuhr [2007]

## Slide 89: Path Search
Flight 1
Flight 2
Flight 4
Flight 5
Flight 3
Flight 6
Flight 7

## Slide 90: Path Search
Flight 1
Flight 2
Flight 4
Flight 5
Flight 3
Flight 6
Flight 7

## Slide 91: Path Search
Flight 1
Flight 2
Flight 4
Flight 5
Flight 3
Flight 6
Flight 7

## Slide 92: Path Search
Flight 1
Flight 2
Flight 4
Flight 5
Flight 3
Flight 6
Flight 7

## Slide 93: Path Search
Flight 1
Flight 2
Flight 4
Flight 5
Flight 3
Flight 6
Flight 7

## Slide 94: Path Search
Flight 1
Flight 2
Flight 4
Flight 5
Flight 3
Flight 6
Flight 7

## Slide 95: Path Search
Flight 1
Flight 2
Flight 4
Flight 5
Flight 3
Flight 6
Flight 7

## Slide 96: Accuracy vs. Speed
Instance SC1: reference solution
  100 legs, 16 aircraft, no preassignments, no maintenace
  Optimizer produces the same solution for each step size
  CPU time differs only in computation of the convolutions
  PDP values differ because of approximation error
  * Comparison with average of 100 000 iterations
 | step size [min] | CPU [s] | PDP | error [%]
SC1 | 0.1 | 15.4 | 25.0586 | 0.11
SC1 | 0.5 | 1.0 | 25.0672 | 0.15
SC1 | 1 | 0.5 | 25.0917 | 0.25
SC1 | 2 | 0.4 | 25.2227 | 0.77
SC1 | 3 | 0.4 | 25.4775 | 1.79
SC1 | 4 | 0.3 | 25.7667 | 2.94
Simulation* |  |  | 25.0303 | 

## Slide 97: Accuracy vs. Speed
Instance SC1: optimized solution
  Different discretization step sizes may produce different solutions
  CPU time and PDP are not straightforward to compare
  *Value is average of 10 000 iterations
 | step size [min] | PDP optimized | CPU [s] | PDP simulated*
SC1 | 0.1 | 19.7268 | 4450 | 19.7469
SC1 | 0.5 | 19.7362 | 231 | 19.7382
SC1 | 1 | 19.7450 | 70 | 19.7239
SC1 | 2 | 19.8693 | 45 | 19.7313
SC1 | 3 | 20.0651 | 29 | 19.7239
SC1 | 4 | 20.3353 | 31 | 19.7562

## Slide 98: Test Instances
Analyzed data
  approx. 350000 flights / 300 – 650 flights per day
  28 months, 4 subfleets
  European airline with hub-and-spoke network
Test instances
  We optimize single day instances of one subfleet
  Data for 4 months, no maintenance rules and preassignments
 |  | min |  |  | max |  |  | avg |  | 
 | #days | Legs | aircraft | flight time [min] | legs | aircraft | flight time [min] | legs | aircraft | flight time [min]
January | 26 | 44 | 12 | 3840 | 105 | 17 | 8830 | 88 | 15 | 7447
February | 22 | 94 | 15 | 8295 | 118 | 17 | 10065 | 109 | 16 | 9339
March | 21 | 94 | 15 | 7900 | 121 | 17 | 10390 | 110 | 16,3 | 9483
April | 27 | 93 | 15 | 7080 | 118 | 18 | 9750 | 103 | 16 | 8648

## Slide 99: Gate Phase
Probability of delay
  Depends on day time and departure airport
Distribution of delay
  Independent of daytime and departure airport
Chart: probability
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60
 | 0.096837 | 0.10826 | 0.11485 | 0.061236 | 0.091005 | 0.063026 | 0.054536 | 0.046194 | 0.040972 | 0.041285 | 0.029271 | 0.024251 | 0.020467 | 0.019268 | 0.019102 | 0.014192 | 0.011646 | 0.0097261 | 0.009154 | 0.010003 | 0.0070316 | 0.0064595 | 0.0059981 | 0.0051307 | 0.0056474 | 0.0044294 | 0.0041156 | 0.0035804 | 0.0035066 | 0.0031375 | 0.0024546 | 0.0028422 | 0.0023439 | 0.0025469 | 0.0021962 | 0.0020301 | 0.0018825 | 0.0018825 | 0.0017717 | 0.0018271 | 0.001661 | 0.0011812 | 0.0011073 | 0.0013657 | 0.0013288 | 0.0013473 | 0.0009966 | 0.001255 | 0.0010151 | 0.0012365 | 0.00090433 | 0.00094124 | 0.00059058 | 0.00055367 | 0.00075668 | 0.00064595 | 0.0006644 | 0.00084896 | 0.00071977 | 0.00079359
 | 0.14548 | 0.16953 | 0.14891 | 0.053608 | 0.079496 | 0.052234 | 0.039404 | 0.037801 | 0.027491 | 0.034135 | 0.020389 | 0.021077 | 0.014662 | 0.012142 | 0.01764 | 0.0089347 | 0.009622 | 0.0084765 | 0.0077892 | 0.010309 | 0.0045819 | 0.0043528 | 0.0036655 | 0.00252 | 0.0052692 | 0.00252 | 0.00252 | 0.0032073 | 0.0016037 | 0.0020619 | 0.0011455 | 0.0013746 | 0.0016037 | 0.00252 | 0.0029782 | 0.0013746 | 0.00045819 | 0.0018328 | 0.00068729 | 0.00252 | 0.00091638 | 0.0013746 | 0.00068729 | 0 | 0.00068729 | 0.0013746 | 0.00091638 | 0.00068729 | 0.00068729 | 0.0018328 | 0.00045819 | 0.0002291 | 0.00091638 | 0.0002291 | 0.0013746 | 0.0002291 | 0.00068729 | 0.0002291 | 0.0002291 | 0
 | 0.10395 | 0.10752 | 0.11288 | 0.085106 | 0.084132 | 0.062693 | 0.05782 | 0.052298 | 0.038655 | 0.039142 | 0.031509 | 0.02485 | 0.019003 | 0.017379 | 0.020465 | 0.015592 | 0.0099074 | 0.0087705 | 0.0076336 | 0.009745 | 0.0061718 | 0.0060094 | 0.0056846 | 0.005847 | 0.0047101 | 0.0051973 | 0.0042228 | 0.0034108 | 0.0027611 | 0.0037356 | 0.001949 | 0.0016242 | 0.001949 | 0.0009745 | 0.0012993 | 0.0024363 | 0.001949 | 0.00081208 | 0.0009745 | 0.0016242 | 0.00081208 | 0.0012993 | 0.00016242 | 0.0009745 | 0.0009745 | 0.0009745 | 0.00064967 | 0.0012993 | 0.00048725 | 0.0011369 | 0.0009745 | 0.00016242 | 0.00048725 | 0.00048725 | 0.00048725 | 0 | 0.00048725 | 0.00032483 | 0.00016242 | 0.00016242
 | 0.08471 | 0.095568 | 0.10947 | 0.074781 | 0.081964 | 0.069754 | 0.062867 | 0.055516 | 0.043137 | 0.038236 | 0.029913 | 0.025096 | 0.021885 | 0.020913 | 0.017618 | 0.01597 | 0.012168 | 0.011112 | 0.0088724 | 0.0092949 | 0.0077739 | 0.0067176 | 0.0061684 | 0.0058304 | 0.0058304 | 0.0039714 | 0.0038869 | 0.0042672 | 0.0032532 | 0.0030842 | 0.0029152 | 0.0029575 | 0.002197 | 0.002197 | 0.0023237 | 0.0019012 | 0.0013942 | 0.0022392 | 0.00169 | 0.0010985 | 0.0016055 | 0.001183 | 0.0012252 | 0.001352 | 0.0012252 | 0.0011407 | 0.00084499 | 0.00071824 | 0.00092949 | 0.0011407 | 0.0013097 | 0.00092949 | 0.00097174 | 0.00063374 | 0.00050699 | 0.00059149 | 0.00059149 | 0.00076049 | 0.00054924 | 0.00063374
 | 0.14195 | 0.13637 | 0.12443 | 0.022098 | 0.18913 | 0.019311 | 0.020307 | 0.017718 | 0.021302 | 0.083615 | 0.012542 | 0.0091579 | 0.0073661 | 0.009357 | 0.039618 | 0.0063707 | 0.0057734 | 0.004778 | 0.0059725 | 0.018515 | 0.0037826 | 0.0019908 | 0.0029863 | 0.002389 | 0.01314 | 0.0021899 | 0.00099542 | 0.0021899 | 0.0015927 | 0.009556 | 0.0011945 | 0.00099542 | 0.0017918 | 0.002389 | 0.0043799 | 0.00039817 | 0.00059725 | 0.00099542 | 0.00059725 | 0.0041808 | 0.00039817 | 0.00039817 | 0.0013936 | 0.00079634 | 0.0031853 | 0.00099542 | 0.00039817 | 0.00059725 | 0.00059725 | 0.0025881 | 0.00059725 | 0.00039817 | 0.00059725 | 0.00099542 | 0.0027872 | 0 | 0.00019908 | 0.00039817 | 0.00039817 | 0.0025881
 | 0.14051 | 0.13786 | 0.13198 | 0.099353 | 0.088477 | 0.063786 | 0.05291 | 0.04321 | 0.035567 | 0.031746 | 0.022634 | 0.016755 | 0.015579 | 0.013815 | 0.013815 | 0.0088183 | 0.0088183 | 0.0064668 | 0.0061728 | 0.0035273 | 0.0044092 | 0.0044092 | 0.0038213 | 0.0023516 | 0.0026455 | 0.0017637 | 0.0029394 | 0.0035273 | 0.0017637 | 0.0023516 | 0.00058789 | 0.0014697 | 0.0014697 | 0.00058789 | 0.0026455 | 0.0011758 | 0.0020576 | 0.00029394 | 0.00029394 | 0.0020576 | 0.00058789 | 0.00088183 | 0.00029394 | 0.00058789 | 0.00029394 | 0 | 0 | 0.00029394 | 0 | 0 | 0.00058789 | 0.00029394 | 0.00029394 | 0 | 0.0014697 | 0 | 0 | 0.00029394 | 0.00029394 | 0.00029394
probability of departure delay during the day on various airports
distribution of the length of gate primary delays on various airports
Gate phase
  gate delay distribution Gj of flight j
where Ln() is probability density function of Log-normal distribution with Power-law distributed tail and , t(j) is departure time of flight j and a(j) is departure airport of flight j

## Slide 100: Flight Phase
Distribution of deviation from scheduled duration
  Depends on scheduled leg duration
Flight phase
  flight delay distribution Fj of flight j
where Llg() is probability density function of Log-logistic distribution and lj is scheduled flight duration of leg j
Histogram of the flight duration and its representation by random variable. left: scheduled flight duration 80 minutes, right: scheduled flight duration 45 minutes
Notes: Tell that they try to fit scheduled flight duration to actual, therefore this agretation is ok.

## Slide 101: Model Verification
Parameters of the model:
  for every airport and day hour
  for every flight length
  Parameters are estimated by automatic scripts in R and quality is proofed by Chi-Square test.
Model applied to South American airline data
Validation of various assumptions of the model
  Stability of parameters over time, …
Notes: Explain pictures and say som other verifications you have done

## Slide 102: Gain of the Method
ORC
  Standard KPI method
  Bonus for ground buffer minutes
  Threshold value for maximal ground buffer time (15 minutes)
PDP
  Total probability of delay propagation
EAD – expected arrival delay
Robust Tail Assignment
102
 |  | ORC |  |  | PDP |  |  | Savings | 
 | #days | PDP | EAD [min] | CPU [s] | PDP | EAD [min] | CPU [s] | PDP | EAD [min]
January | 26 | 414,51 | 28488 | 28 | 395,46 | 28085 | 66 | 19,05 | 403
February | 22 | 540,48 | 31870 | 31 | 530,42 | 31652 | 89 | 10,06 | 218
March | 21 | 516,69 | 30363 | 31 | 507,91 | 30174 | 75 | 8,78 | 189
April | 27 | 465,48 | 34453 | 42 | 449,16 | 34159 | 71 | 16,51 | 294
Notes: Vysvetli savings a pokracuj QQplotom

## Slide 103: Gain in Detail
Estimation of monetary savings by the cost model developed based on EUROCONTROL [2004]
Lufthansa Systems estimates annual saving of the method in the tail assignment to 300,000 € for short haul carrier with 30 aircraft
Application in other planning stages may increase the benefit
ORC vs. PDP on a single disruption scenario
  ORC outperforms PDP only in 21% of cases
  PDP saves on average 29 minutes of arrival delay
  For more disrupted days, PDP saves on average 62 minutes of arrival delay

## Slide 104: Planning in Public Transport (Product, Project, Planned)
B3
Cost Recovery
Fares
Construction Costs
Network Topology
Velocities
Lines
Service Level
Frequencies
Connections
Timetable
Sensitivity
Rotations
Relief Points
Duties
Duty Mix
Rostering
Fairness
Crew Assignment
Disruptions
Operations Control
multidepartmental
Departments
multidepotwise
Depots
multiple line groups
Line Groups
multiple lines
Lines
multiple rotations
Rotations
B1
AN-OPT/B5
BS-OPT
IS-OPT
VS-OPT
DS-OPT
APD
B1
VS-OPT2
B15

## Slide 105: Visit ISMP 2012!

## Slide 106: Thank your for your attention
PD Dr. habil. Ralf Borndörfer Zuse-Institute Berlin Takustr. 7 14195 Berlin-Dahlem Fon (+49 30) 84185-243 Fax (+49 30) 84185-269 borndoerfer@zib.de www.zib.de/borndoerfer